## Slide 1: 19CS211 Computer Organisation and Architecture Session 4 (12-01-2021) Dr V Anantha Narayanan

## Slide 2: Big / Little Endian

## Slide 5
A load word or store word instruction uses only one memory address. The lowest address of the four bytes is used for the address of a block of four contiguous bytes.
How is a 32-bit pattern held in the four bytes of memory? There are 32 bits in the four bytes. A choice has to be made about which byte of memory gets what part of the pattern. There are two ways that computers commonly do this:
32-bit pattern 0x12345678 is stored at address 0x00400000. The most significant byte is 0x12; the least significant is 0x78.
Within a byte the order of the bits is the same for all computers (no matter how the bytes themselves are arranged).

## Slide 6
Big Endian Byte Order: The most significant byte (the "big end") of the data is placed at the byte with the lowest address. The rest of the data is placed in order in the next three bytes in memory. 32 Bit data 0x12345678 and Address is 0x04000000
0x04000000 | 0x04000001 | 0x04000002 | 0x04000003
12 (MSB) | 34 | 56 | 78 (LSB)

## Slide 7
Little Endian Byte Order: The least significant byte (the "little end") of the data is placed at the byte with the lowest address. The rest of the data is placed in order in the next three bytes in memory. 32 Bit data 0x12345678 and Address is 0x04000000
0x04000000 | 0x04000001 | 0x04000002 | 0x04000003
78 (LSB) | 56 | 34 | 12 (MSB)

## Slide 9
Which ordering is better ?
• The ordering has absolutely no effect of processor performance and any other performance factor.
As long as the processor retrieve the bytes stored in the memory in the same ordering as the processor stores the bytes, the load and store instructions will operate correctly and with the same efficiency

## Slide 10
The endianness in use is determined by the CPU type.
For example:
The INTEL processors (x86) are little endian
The ARM processor is little endian by default; and can be programmed to operate as big endian
Many older processors were big endian, such as: Motorola M68000 and SPARC

## Slide 11: Performance Metrics

## Slide 12
The speed of a computer processor, or CPU, is determined by the clock cycle, which is the amount of time between two pulses of an oscillator. Generally speaking, the higher number of pulses per second, the faster the computer processor will be able to process information. The clock speed is measured in Hz, typically either megahertz (MHz) or gigahertz (GHz). For example, a 4GHz processor performs 4,000,000,000 clock cycles per second.

## Slide 14
The time required by the microprocessor to complete an operation of accessing memory or input/output devices is called machine cycle.
One time period of frequency of microprocessor is called t-state.
A t-state is measured from the falling edge of one clock pulse to the falling edge of the next clock pulse. Here, Fetch cycle takes four t-states and execution cycle takes three t-states.

## Slide 16
Four steps of Machine cycle
Fetch - Retrieve an instruction from the memory.
Decode - Translate the retrieved instruction into a series of computer commands.
Execute - Execute the computer commands.
Store - Send and write the results back in memory.

## Slide 17: Instruction Cycle
The sequence of operations that the CPU has to carry out for execution of an Instruction is called instruction cycle.
1:- Read an Instruction
2:- Decode the instruction
3:- Find the address of operand
4:- retrieve an operand
5:- perform desired operation
6:- find the address of destination
7:- store the result into the destination

## Slide 19
Examples

## Slide 20
Frequency

## Slide 21
Example

## Slide 22
Example
Assume machine A has 5MHz Crystal and Machine B has 10 MHz Crystal
What is the Time of T state in machine B
0.1uS
What is the Time taken by the Instruction MVI A, #35 in Machine B
0.7uS
Which Machine is having better performance
Machine B is having Better performance compared to Machine A

## Slide 23: End of Session 4