## Slide 1: Fast Adders
Lectures 28 & 29

## Slide 2: Contd.
The final result of the addition will be valid after a delay of n Δ t, which is equal to 2n gate delays.
In addition to the delay in the ripple-carry path, there is also a delay in the XOR gates that feed either the true or complemented value of Y to the adder inputs.
If this delay is equal to one gate delay, then the total delay is 2n + 1 gate delays.
For a large n, say n = 32 or n = 64, the delay would lead to unacceptably poor performance.
Therefore, it is important to find faster circuits to perform addition.
The speed of any circuit is limited by the longest delay along the paths through the circuit.
  In this case, the longest delay is along the path from the yi input, through the XOR gate and through the carry circuit of each adder stage.
  The longest delay is often referred to as the critical-path delay, and the path that causes this delay is called the critical path.

## Slide 3: Fast Adders
The performance of a large digital system is dependent on the speed of circuits that form its various functional units.
  It can be improved by changing the overall structure of a functional unit.
The ripple-carry adder has 2n+1 gate delays, so we need faster adders
1 Bit Full Adder

## Slide 4: Contd.
To reduce the delay caused by the effect of carry propagation through the ripple-carry adder, we can attempt to evaluate the carry-in from the previous stage quickly.
If a correct evaluation can be made in a relatively short time, then the performance of the complete adder will be improved.
The carry-out function for stage i can be realized as
ci+1 = xiyi + xici + yici
If we factor this expression as
ci+1 = xiyi + (xi + yi)ci
Then it can be written as
ci+1 = gi + pici (1)
where
gi = xiyi
pi = xi + yi

## Slide 5: Carry-Lookahead Adder
The function gi is equal to 1 when both inputs xi and yi are equal to 1, regardless of the value of the incoming carry to this stage, ci .
  Since in this case, stage i is guaranteed to generate a carry-out, g is called the generate function. (Because both xi and yi are 1)
The function pi is equal to 1 when at least one of the inputs xi and yi is equal to 1.
  In this case a carry-out is produced if ci = 1.
  The effect is that the carry-in of 1 is propagated through stage i; hence pi is called the propagate function.
Now rewriting ci+1 using carry for stage i − 1 we get,
ci+1 = gi + pi(gi−1 + pi−1ci−1)
= gi + pigi−1 + pipi−1ci−1
The same expansion for other stages, ending with stage 0, gives
ci+1 = gi + pigi−1 + pipi−1gi−2 +· · ·+pipi−1 · · · p2p1g0 + pipi−1 · · · p1p0c0
This expression represents a two-level AND-OR circuit in which ci+1 is evaluated very quickly.
An adder based on this expression is called a carry-lookahead adder.

## Slide 6: Contd.
Figure shows the first two stages of a ripple-carry adder.
In each stage, an extra OR gate is used (which produces the pi signal), instead of an AND gate
  because we factored the sum-of-products expression for ci+1.
The slow speed of the ripple-carry adder is caused by the long path along which a carry signal must propagate.
Here, the critical path is from inputs x0 and y0 to the output c2.
  It passes through five gates, as highlighted in pink.
  The path in other stages of an n-bit adder is the same as in stage 1.
  Therefore, the total number of gate delays along the critical path is 2n + 1.
A ripple-carry adder based on expression 1

## Slide 7: The first two stages of a carry-lookahead adder.
Figure gives the first two stages of the carry-lookahead adder, using expressions to implement the carry-out functions.
Thus
c1 = g0 + p0c0
c2 = g1 + p1g0 + p1p0c0
This circuit does not have the long ripple-carry path.
Instead, all carry signals are produced after three gate delays:
  one gate delay is needed to produce the generate and propagate signals g0, g1, p0, and p1, and
  two more gate delays are needed to produce c1 and c2 concurrently.

## Slide 8: Contd.
Extending the circuit to n bits, the final carry-out signal cn would also be produced after only three gate delays
  because of the two-level (AND-OR) circuit.
The total delay in the n-bit carry-look ahead adder is four gate delays.
  The values of all gi and pi signals are determined after one gate delay. It takes two more gate delays to evaluate all carry signals.
  Finally, it takes one more gate delay (XOR) to generate all sum bits.
The key to this good performance of the adder is quick evaluation of carry signals.

## Slide 9: Hierarchical carry-look ahead adder
But, the complexity of an n-bit carry-look ahead adder increases rapidly as n becomes larger.
To reduce the complexity, we can use a hierarchical approach in designing large adders.
Suppose that we want to design a 32-bit adder. We can divide this adder into 4 eight-bit blocks, such that
  block 0 adds bits 7 . . . 0, block 1 adds bits 15 . . . 8,
  block 2 adds bits 23 . . . 16, and block 3 adds bits 31 . . . 24.
Then we can implement each block as an eight-bit carry-look ahead adder.
The carry-out signals from the four blocks are c8, c16, c24, and c32.
Now we have two possibilities. 1) We can connect the four blocks as four stages in a ripple-carry adder. Or 2) We can also have carry lookahead between blocks

## Slide 10: Hierarchical carry-look ahead adder with ripple-carry between blocks
Here while carry-lookahead is used within each block, the carries ripple between the blocks.

## Slide 11: Hierarchical carry-look ahead adder.
Instead of using a ripple-carry approach between blocks, a faster circuit can be designed in which
  a second-level carry-look ahead is performed to produce quickly the carry signals between blocks as below,
Each block in the top row includes an eight-bit carry-look ahead adder, based on generate and propagate signals for each stage in the block, as discussed before.
However, instead of producing a carry-out signal from the most-significant bit of the block, each block produces generate and propagate signals for the entire block.
  Let Gj and Pj denote these signals for each block j.
Now Gj and Pj can be used as inputs to a second-level carry look ahead circuit at the bottom of circuit, which evaluates all carries between blocks.

## Slide 12: Contd.
We can derive the block generate and propagate signals for block 0 by examining the expression for c8
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4g3 + p7p6p5p4p3g2
+ p7p6p5p4p3p2g1 + p7p6p5p4p3p2p1g0 + p7p6p5p4p3p2p1p0c0
The last term in this expression specifies that, if all eight propagate functions are 1, then the carry-in c0 is propagated through the entire block.
Hence, P0 = p7p6p5p4p3p2p1p0
The rest of the terms in the expression for c8 represent all other cases when the block produces a carry-out.
Thus, G0 = g7 + p7g6 + p7p6g5 +· · ·+p7p6p5p4p3p2p1g0
The expression for c8 in the hierarchical adder is given by
c8 = G0 + P0c0

## Slide 13: Contd.
For block 1 the expressions for G1 and P1 have the same form as for G0 and P0 except that each subscript i is replaced by i + 8.
The expressions for G2, P2, G3, and P3 are derived in the same way.
The expression for the carry-out of block 1, c16, is,
c16 = G1 + P1c8 = G1 + P1G0 + P1P0c0
Similarly, the expressions for c24 and c32 are
c24 = G2 + P2G1 + P2P1G0 + P2P1P0c0
c32 = G3 + P3G2 + P3P2G1 + P3P2P1G0 + P3P2P1P0c0
Using this scheme, it takes two more gate delays to produce the carry signals c8, c16, c24, and c32 than the time needed to generate the Gj and Pj functions.

## Slide 14: Contd.
Therefore, since Gj and Pj require three gate delays, c8, c16, c24, and c32 are available after five gate delays.
The time needed to add two 32-bit numbers involves these five gate delays plus two more to produce the internal carries in blocks 1, 2, and 3, plus one more gate delay (XOR) to generate each sum bit.
This gives a total of eight gate delays.
But it had taken 2n + 1 gate delays to add two numbers using a ripple-carry adder.
  For 32-bit numbers this implies 65 gate delays.
Thus, it is clear that the carry-look ahead adder offers a large performance improvement with a trade-off of much greater complexity of the required circuit.

## Slide 15: Technology Considerations
The preceding delay analysis assumes that gates with any number of inputs can be used. But, the number of gate inputs, referred to as the fan-in of the gate, has to be limited in practice.
  Fan-in is the number of inputs to the gates
  Fan-out is the number of gates driven by the gate
Therefore the reality of fan-in constraints must be taken into account.
To illustrate this problem, consider the expressions for the first eight carries:
c1 = g0 + p0c0
c2 = g1 + p1g0 + p1p0c0
……...
c8 = g7 + p7g6 + p7p6g5 + p7p6p5g4 + p7p6p5p4g3 + p7p6p5p4p3g2 + p7p6p5p4p3p2g1 + p7p6p5p4p3p2p1g0 + p7p6p5p4p3p2p1p0c0

## Slide 16: Contd.
Suppose that the maximum fan-in of the gates is four inputs. Then it is impossible to implement all of these expressions with a two-level AND-OR circuit.
The biggest problem is c8, where one of the AND gates requires nine inputs; moreover, the OR gate also requires nine inputs.
To meet the fan-in constraint, we can rewrite the expression for c8 as
c8 = (g7 + p7g6 + p7p6g5 + p7p6p5g4) + [(p7p6p5p4)(g3 + p3g2 + p3p2g1 + p3p2p1g0)] + ( p7p6p5p4)( p3p2p1p0)c0
To implement this expression we need 11 AND gates and 3 OR gates.
The propagation delay in generating c8 consists of one gate delay to develop all gi and pi,
  two gate delays to produce the sum-of-products terms in parentheses,
  one gate delay to form the product term in square brackets, and
  one delay for the final ORing of terms.

## Slide 17: Contd.
Hence c8 is valid after five gate delays, rather than the three gate delays that would be needed without the fan-in constraint.
Because fan-in limitations reduce the speed of the carry-lookahead adder, some devices that are characterized by low fan-in include dedicated circuitry for implementation of fast adders.
  Examples of such devices is FPGA (Field Programmable Gate Array).

## Slide 18: An alternative design for a carry-lookahead adder
The same functionality of carry lookahead adder can be achieved by using the circuit in Figure.
In this case stage 0 is implemented such that 2 two-input XOR gates are used to generate the sum bit, rather than having 1 three-input XOR gate.
The output of the first XOR gate can also serve as the propagate signal p0.
Thus the corresponding OR gate is not needed.
Stage 1 is constructed using the same approach.